## Slide 1
HỌC VIỆN CÔNG NGHỆ BƯU CHÍNH VIỄN THÔNG
COMPUTER ARCHITECTURE
Instructor: Associate Professor Phạm Văn Cường
E-mail: cuongpham.ptit@gmail.com
www: https://sites.google.com/view/cuongpham/home
CENTRAL PROCESSING UNIT

## Slide 2: CHAPTER 2: CENTRAL PROCESSING UNIT
CPU diagram
Instruction execution
Registers
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Internal bus
Examples

## Slide 3: CPU DIAGRAM
CU: Control Unit
IR: Instruction Register
PC: Program Counter
MAR: Memory Address Register
MBR: Memory Buffer Register
A: Accumulator Register
Y, Z: Temporary Register
FR: Flag Register
ALU: Arithmetic and Logic Unit
CU
IR
PC
MAR
MBR
Internal Bus
A
Y
ALU
Z
FR
A Bus
D Bus

## Slide 4: INSTRUCTION EXECUTION
Operating System loads the program code into the memory;
Program Counter (PC) = address of the memory cell that stores the 1st instruction of the program;
MAR = PC then uploaded to bus A;
Bus A passes the cell address to MMU - Memory Management Unit;
MMU selects and reads data from the cell;
Instruction code or data (stored on the cell) is uploaded on bus D and then stored on the MBR register;

## Slide 5: INSTRUCTION EXECUTION
MBR transfers the instruction code to IR (as an input for CU);
CU decodes the instruction code, and generates the control signals and send them to other components (such as ALU), for making the instruction be executed;
PC is increased by 1 and points to the memory cell that is stored the next instruction to be executed;
Repeat step 3rd -9th for all instructions of program.

## Slide 6: CPU registers
Act as memory cells, registers can:
  Temporarily store instructions and data to be processed by CPU;
  Small size;
  High-speed access
CPU can have tens (80x86) to hundreds of registers;
Size can vary 8, 16, 32, 64, 128 and 256 bits:
  8086-80286: 8 and 6 bit
  80386-Pentium II: 16-32 bit
  Pentium 4, Core Duo: 32, 64 and 128 bit.

## Slide 7: Accumulator (A)
Present in most CPU, A can be used for:
  Storing the input operands
  Storing the results
  Communicating between CPU and I/O devices
Sized can be: 8, 16, 32 and 64 bit.

## Slide 8: Program Counter
Program Counter (PC) or so-called IP(Instruction Pointer) contains the address of memory cell stored the next instruction to be executed;
When a program is activated, PC contains the address of the memory storing the first instruction of the program;
Size of PC can vary 8, 16, 32 or 64 bits.

## Slide 9: Flag Register (FR)
Stores the status of CPU in which each bit presents a “flag” derived from the computation output of ALU;
Two types of flags:
  Status flags: CF, OF, AF, ZF, PF, SF
  Control flags: IF, TF, DF
Flags often are used for branch or condition in the program;
Size of FR relies on the design of CPU.

## Slide 10: Flag Register
ZF: Zero flag, ZF=1 if result (from ALU)=0 and ZF=0 if result <>0.
SF: Sign flag, SF=1 if result is negative. SF=0 otherwise.
CF: Carry flag, CF=1 if carried, CF=0 otherwise.
AF: Auxilary flag, AF=1 if carried of an addition or borrowing of a subtraction to/from lower nibble (four lower bits).
OF: Overflow flag, OF=1 if overflow, OF=0 otherwise.
PF: parity flag, PF=1 if the sum of bits ‘1’ is odd, and PF=0 if the sum of bits ‘1’ is even.
IF: Interrupt flag, IF=1: interrupt enable, IF=0: interrupt disable .

## Slide 11: 8086’s FR

## Slide 12: Stack Pointer (SP)
Stack works under last in first out (LIFO) rule;
SP contains the address of the top of the stack;
Two operations:
  Push:
    SP  SP + 1
    {SP}  Data
  Pop:
    Register  {SP}
    SP  SP - 1
SP
Stack

## Slide 13: General Purpose Registers
General Purpose Registers are registers used for multi purposes:
Examples: CPU Intel 8086 has four general purpose registers:
  AX: Accumulator register
  BX: Base register
  CX: Counter register
  DX: Data register

## Slide 14: Instruction Register
Instruction register (IR) store op-code being executed;
IR loads an op-code from MBR and pass it to CU for decoding and executing.
MBR
IR
CU

## Slide 15: MAR and MBR
MAR – (Memory address register):
  Interface between CPU and bus A
  Receive cell memory address from PC and pass it to bus A.
MBR –(Memory buffer register):
  Interface between CPU and bus D
  Receive op-code from bus D and pass it to IR through internal bus in CPU.

## Slide 16: Temporary Registers
Temporary registers can be used for:
  Storing input operants
  Storing output results
  Concurrent execution
  Out Of Order execution (OOO)

## Slide 17: Control Unit
Control Unit CU
IR
CLK
ALU Flags
Internal control signal
External control signal

## Slide 18: Control Unit
Control Unit controlizes operations of CPU using CPU clock cycles;
CU’s inputs:
  Op-code stored in IR
  FR
  Clock cycles
CU’s outputs:
  Controlizes units inside CPU;
  Controlizes units outside CPU
CU generizes clock cycles for synchronizing units inside and outside CPU.

## Slide 19: Arithmetic Logic Unit (ALU)
ADD
SUB
MUL
DIV
SHR
ROL
OR
NOT
AND
XOR
SHL
NEG
ROR
IN
IN
OUT

## Slide 20: ALU
ALU (Arithmetic and Logic Unit) comprises of computing sub-units:
  ADD, SUB, MUL, DIV
  SHIFT, ROTATE
  NOT, AND, OR, XOR
ALU has
  Two inputs (registers);
  One output: to transfer computation results to registers.

## Slide 21: Internal Bus
A channel for communicating among units inside of CPU (CU – Registers – ALU);
full duplex
Interfacing between internal and system bus;
Has high-speed broadband (much more than system bus).

## Slide 22: Intel 8086

## Slide 23: AMD K62

## Slide 24: AMD K62

## Slide 25: Intel Pen III

## Slide 26: Intel Pen IV

## Slide 27: AMD Athlon XP

## Slide 28: Intel Core 2 Duo

## Slide 29: Nehalem used in Intel Core i5/i7 (2008)

## Slide 30: Sandy Bridge used in Intel Core i5/i7 (2010)

## Slide 31: Introduction to pipeline

## Slide 32: CPU pipeline
No pipeline
pipeline

## Slide 33: CPU pipeline
An instruction is executed within 5 steps
5 steps:
  Instruction Fetch - IF
  Instruction Decode - ID
  Execute - EX
  Memory Access - MEM:
  Write Back - WB:

## Slide 34: CPU pipeline’s hardware

## Slide 35: Pipeline hazards
Resource conflicts
  Memory access
  Register access
Data hazards
Branch instructions
  Unconditional jumps
  Conditional jumps
  Call and return

## Slide 36: Data hazards and solutions

## Slide 37: Pipeline example – P6 (PIII, M)

## Slide 38: Resource hazards
insufficient computing resource;
If memory allows one access at one time, but there are two or more accesses, pipeline requests two memory accesses (i.e. IF and ID)  memory hazard.

## Slide 39: Branch hazards
Branch dominates about 10-30% of instructions. Branch can cause the following issues:
  Interruption of program execution;
  Make the pipeline be emptied.
The more pipeline stages, the more complicated is (i.e. more paralleled instruction executions) :
  The pipeline bubbles need to be filled out;
  Branch prediction.

## Slide 40: Branch hazard example

## Slide 41: Branch hazard example
Code example:
    ADD R2, R3, R4
    CMP R1,0
    JNE somewhere
Insert NO-OP right below the branch
    ADD R2, R3, R4
    CMP R1,0
    JNE somewhere
    NO-OP
Move the independent instructions to right before the branch:
    CMP R1,0
    JNE somewhere
    ADD R2, R3, R4