## Slide 1
HỌC VIỆN CÔNG NGHỆ BƯU CHÍNH VIỄN THÔNG
COMPUTER ARCHITECTURE
Instructor: Associate Professor Phạm Văn Cường
E-mail: cuongpham.ptit@gmail.com
www: https://sites.google.com/view/cuongpham/home
CACHE & MEMORY

## Slide 2: Agenda
Introduction to hierarchical memory
Memory classification
  - ROM
  - RAM
Cache Memory

## Slide 3: Hierarchical model

## Slide 4: Figures

## Slide 5: Memory system
CPU registers:
  Small size, few bytes to few KB
  High speed access (0,25ns)
  Expensive
Cache memory:
  Small capacity (8KB to 32MB)
  High speed access (1-5ns)
  Expensive
  So called smart memory
  Store opcode and data to be processed by CPU.

## Slide 6: Memory system
Main memory:
  ROM and RAM, large size, about 256MB to 16GB
  Low-speed access (50 to 70ns)
  Cheap
  Store opcode and data of systems and users.
Secondary memory:
  Very large capacity, from few GB to few TB
  Very slow speed access (5ms)
  Very cheap
  Store data (files).

## Slide 7: Why hierarchical memory ?
Performance improvement
  Balancing between high-speed processing of CPU and low-speed processing of main memory and secondary memory;
Cost reduction
  Expensive memories such as registers and cache can be used with a small amount;
  Cheap memories such as main memory and secondary memory are used with large amount;
   Sum of costs will be reduced.

## Slide 8: Memory classification
Access types:
  Random Access Memory (RAM)
  Serial Access Memory (SAM)
  Read Only Memory (ROM)
Volatile types:
  Volatile memory (RAM): data are removed if the power supply is off.
  Non-volatile memory (ROM, HDD)
Manufacture technology:
  Semiconductor memory: ROM, RAM
  Magnetic memory: HDD, FDD, tape
  Optical memory: CD, DVD

## Slide 9: Memory circuit organization

## Slide 10: ROM
Read Only Memory
  Data are written in ROM using specialized technology;
ROM is a stable memory
  Information stored in ROM is not losing even power supply is off
ROM is a semi-conductor memory; each cell is a semi-conductor gate
ROM is usually stored system information:
  BIOS (Basic Input Output System).

## Slide 11: ROM example

## Slide 12: RAM
RAM (Random Access Memory)
  Each cell in RAM can randomly be accessed;
  Access speed for all memory cells are equal.
RAM is not a stable:
  Information stored in RAM is removed when power supply is off
RAM is a semi-conductor memory
RAM stores information of systems and users
Notes: f

## Slide 13: RAM examples
SDRAM PC133
DDR3 1066 SDRAM

## Slide 14: Cache memory
What is Cache?
Cache principles
Hit rate and miss rate
Cache architecture
Cache organization
Read/Write
Replication policies

## Slide 15: What is a Cache?
Cache is a smart memory:
  Cache is in between main memory and CPU;
Cache:
  is positioned out of CPU (old systems)
  Is integrated inside CPU.
CPU
Cache
Main memory

## Slide 16: Cache
Performance improvement
  Balanced between high-speed CPU and low-speed main memory;
  Reducing time for access data and instructions.
Cost reduction
  Two computer systems have the same cost, the one with cache has higher speed access than the other;

## Slide 17: Principles
Cache is call a smart memory:
  Cache is able to predict data and instructions need to be executed by CPU;
  Access data in cache is fast.
Two principles:
  Spatial locality
  Temporal locality

## Slide 18: Examples
  Spatial locality
  If a memory cell is accessed, its neighbors can be highly likely accessed;
  Array, linked list etc.
  Access by blocks
Neighbour cell
Current cell
Neighbour cell

## Slide 19: Example
  Temporal locality
  If a memory cell has been accessed, it would be highly likely accessed again;
Loop, branch
Instruction 1
Instruction 2
Instruction 3
Instruction 4
Instruction 5
End of loop
Start of loop

## Slide 20: 4.5.4 Data exchange among CPU-Cache-Mem
CPU read/write individual data items from/to cache
Cache read/write data blocks (multiple words) from/to main memory
  why?
CPU
Cache
Memory
Individual data items: byte, word
Block of data: 16, 32, 64 bytes
Notes: D08CN5 4.3, D08CN4 9.3

## Slide 21: hit and miss
Hit: CPU accesses a data item that is available in cache:
  Probability of a hit called hit rate (standed for H).
  0 <= H <= 1
  The bigger hit rate, the higher performance of the cache.
Miss CPU accesses a data item that is unavailable in cache:
  Probability of a miss called miss rate, 1-H.
  0 <= (1 – H) <= 1
  The lower miss rate, the less performance of the cache.
Notes: D08CN6 4.3

## Slide 22: Cache architecture – Look aside
Cache controller
Tag RAM
SRAM
Main Memory
CPU
System bus
Cache and main memory share the system buses;
Advantages:
  Simple design
  Quick Miss
Disadvantages:
  Slow hit

## Slide 23: Cache’s architecture – Look through
Cache is in between CPU and main memory;
Advantages:
  Fast Hit
Disadvantages:
  Complex design
  Expensive
  Slow Miss
Tag RAM
Main Memory
CPU
Cache controller
SRAM

## Slide 24: Cache organization
How cache and main memory can communicate?

## Slide 25: Cache organization
Direct mapping
  Fast and simple
  “Hard” mapping, more conflicted
Fully associative mapping
  Slow and complex
  “Soft” mapping, less conflicted
Set associative mapping
  Fast and complex
  “Soft” mapping, less conflicted

## Slide 26: Direct mapping
Line n-1
Line 1
Line 0
Cache
Memory
Line n-1
Line 1
Line 0
Page 0
Page 1
Page m-1

## Slide 27: Direct mapping
Cache:
  Partitioned into n blocks or lines Line0 to Linen-1
Memory:
  Partitioned into m pages, page0 to pagem-1.
  Each page sizes equally to cache (each page has n lines)
Mapping:
  Line0 of {page0 …pagem-1} is mapped to cache’s line0
  Line1 of {page0 …pagem-1 } is mapped to cache’s line1;
  ....
  Linen-1 of {page0 …pagem-1} is mapped to cache’s Linen-1;

## Slide 28: Direct mapping
Advantages:
  Simple design
  Fast.
Disadvantages:
  Highly conflicted
  Low hit rate.

## Slide 29: Fully associative mapping
Line n-1
Line 1
Line 0
Cache
Memory
Line m-1
Line 1
Line 0

## Slide 30: Fully associative mapping
Cache:
  Partitioned into n lines Line0 to Linen-1
Memory:
  Partitioned into m lines Line0 to Linem-1.
  Sizes of cache’s lines and memory’s lines are equal
  m is much greater than n (m >> n).
Mapping:
  Each line in memory can be mapped into any line in cache;

## Slide 31: Fully associative mapping
Advantages:
  Reduce conflicts
  Hit rate is higher than direct mapping.
Disadvantages:
  Slow due to time taken for finding data in cache
  Complex due to address decoding.
Only suitable for small caches.

## Slide 32: Set associative mapping
Line n-1
Line 1
Line 0
Cache
Bộ nhớ
Line n-1
Line 1
Line 0
Page 0
Page 1
Page m-1
Line n-1
Line 1
Line 0
Way 0
Way 1

## Slide 33: Set associative mapping
Cache:
  Partitioned into k way (same sizes);
  Each way has n lines, Line0 to Linen-1
Memory:
  Partitioned into m pages, page0 to pagem-1.
  Page size equals to cache’s way size
  Each page has n lines, Line0 to Linen-1
Mapping:
  Page is mapped to any way (flexible):
    Each page can be mapped onto any way in cache.
  Mapping from fine in memory to line in way is fixed:
    Linek of pagei is mapped into Linek of wayj;

## Slide 34: Set associative mapping
Advantages:
  Fast (as direct mapping);
  Reduce conflicts.
  High hit rate.
Disadvantages:
  Complex (design and control).

## Slide 35: Cache’s lines replacement
Why?
  Mapping between memory to cache is many-to-one;
  Many lines in memory share one line in cache.
Replacement is to determind which line in cache is replaced with lines from memory.
Replacement policies :
  Random
  First in first out (FIFO)
  Least Recently Used (LRU).

## Slide 36: Cache performance
Access time (taccess) of a cache-memory system:
  taccess = (Hit cost) + (miss rate) * (miss penalty)
  taccess = tcache + (1 - H) * (tmemory)
  H is the hit-rate, tcache is cache access time, tmemory is memory access time.
  If tcache = 5ns, tmemory = 60ns và H=80%, then:
  taccess = 5 + (1 – 0.8) * (60) = 5+12 = 17ns
  If tcache = 5ns, tmemory = 60ns và H=95%, then:
  taccess = 5 + (1 – 0.95) * (60) = 5+3 = 8ns