## Slide 1
HỌC VIỆN CÔNG NGHỆ BƯU CHÍNH VIỄN THÔNG
COMPUTER ARCHITECTURE
Interface programming
Instructor: Associate Professor Phạm Văn Cường
E-mail: cuongpham.ptit@gmail.com
www: https://sites.google.com/view/cuongpham/home

## Slide 2: CONTENT
CPU spin signals
CPU-memory interfacing
I/O Interface programming

## Slide 3: 8088 spin signals
8088 has 40 spin signals:
  Address:
    AD0-AD7: shared with bus D;
    A8-A15; A16/S3-A19/S6;
  Data:
    AD0-AD7: shared with bus A và bus D;
    ALE=0data, ALE=1address.
  Control:
    others

## Slide 4: Memory decoding using logical circuits
Memory ROM 2K8
Address range: FF800FFFFF
Bits used for addressing cells within the chip ROM 2K: 11bit (A0-A10).
Bits for chip select
  A19…A16A15A12A11
  1111 1111 1000 0000 0000  1111 1111 1111 1111 1111
CS = RD OR NOT((A19…A16A15A12A11)AND(IO/M))
NOT AND

## Slide 5: Memory decoding using logic circuits
Notes: D08.1 6.9

## Slide 6: Memory decoding using 74LS138

## Slide 7: Memory decoding using 74LS138
74LS138

## Slide 8: Memory decoding using 74LS138
Memory EPROM 4K8
Address range: F8000FFFFF (32KB)
Address signals used for addressing cells in chip EPROM 4K: 12bit (A0-A11).
Address signals used for chip select : A19…A16A15…..A12
  A12A13A14 can be changed while A15-A19 are unchanged (=1).
   Connect A12A13A14 to A, B, C respectively; A15-A19 and IO/M connected to (G2A, G2B).

## Slide 9: Memory decoding using 74LS138

## Slide 10: CPU-I/O interfacing
I/O controller
Buffer reg.
Status reg.
I/O protocol
Data
Address
Control
CPU
Input ports
Output ports
I/O
Notes: D08.3 5.9

## Slide 11: Keyboard-CPU

## Slide 12: Keyboard-CPU
16 keys:
  74LS374 for row and 74LS244 for column;
How to determine of a key is pressed: scan rows and read columns. If a key is pressed than Di = 0.

## Slide 13: Example code
Code to check if key C (row D0, column D3) is pressed. Port address for row is 0Ah and port for column is 0Bh.
Hang EQU 0AH ; row port address
Cot EQU 0BH ; column port address
MOV AL,11111110b ; D0=0 – scan row 0
OUT Hang, AL
Ktra: IN AL, Cot ; read the column port
AND AL,00001000b ; check D3 ( key C)
JNZ Ktra ; not pressed yet
... ; pressed

## Slide 14: LED interface
7447 and LED interfacing:
  Port A: address 0AH, receives the control signals (ON/OFF).
  Port B: address 0BH, receives the number to be displayed on LED in BCD format.
  Turn LED i ON : send Di = 0 to port A
  Turn LED i OFF: send Di = 1 to port A
  Display the number n: send n to port B, then turn LED i ON.

## Slide 15: LED

## Slide 16: LED interfacing

## Slide 17: Example code
Code to display 8 on all 7 LEDs. Control port is 0Ah and data port is 0Bh.
DK_LED EQU 0AH ; Cổng điều khiển LED
DL_LED EQU 0BH ; Cổng dữ liệu hiển thị
MOV AL,FFH ; Tắt tất cả các LED
OUT DK_LED, AL
MOV CX,64 ; Trễ bằng 64 lệnh NOP
Tre: NOP
LOOP Tre
MOV AL,8 ; Đưa số 8 ra 7447
OUT DL_LED,AL
XOR AL,AL ; Đặt AL=0
OUT DK_LED,AL ; Bật tất cả các LED