## Slide 1
HỌC VIỆN CÔNG NGHỆ BƯU CHÍNH VIỄN THÔNG
COMPUTER ARCHITECTURE
Instructor: Associate Professor Phạm Văn Cường
E-mail: cuongpham.ptit@gmail.com
www: https://sites.google.com/view/cuongpham/home
I/O INTERFACING METHODS

## Slide 2: Content
Introduction
Polling
Interrupt
Direct Memory Access

## Slide 3: Introduction
Why I/O:
  Interfacing between CPU and other devices
  Providing data stream for CPU
  Providing sevices for CPU outputting data
methods:
  polling
  Interrupt
  DMA-Direct Memory Access

## Slide 4: Ports
  PS/2: for keybooard and mouse
  COM: serial port
  LPT: parallel port
  IDE, SATA, SCSI: for hard drives
  LAN: for local network card
  Audio: for speaker, mic vnd line-in
  Video: for monitor
  DVI : for digital monitor
  USB:
    USB 1.0: 12Mb/s
    USB 2.0: 480Mb/s
    USB 3.0: 1.5Gb/s

## Slide 5: Polling
  CPU manages devices and port addresses;
  CPU scans devices for checking if they are ready:
    If one device is ready, data are exchanged;
  CPU is controlling during data exchange process

## Slide 6: Polling
Advantages:
  Simple, easy to deploy
  Can be programmable
Disadvantages:
  Low-effectiveness as time-consuming for polling
  Non-feasible for too many devices
Applications:
  System starting up: CPU checks device for configurations
  New devices plugged into the system

## Slide 7: Non-priority polling
Three devices A, B, C
CPU scans all devices in a polling cycle
CPU can exchange one more devices within a polling cycle
Devices are scanned one by one.
Start
A Ready?
Exchange data with A
Yes
No
B Ready?
Exchange data with B
Yes
No
C Ready?
Exchange data with C
Yes
No

## Slide 8: priority polling
Three devices A, B, C in order of priority A, B, C;
CPU can scan all devices in a polling cycle
CPU can only exchange data at most one device within a polling cycle
Device with high priority is firstly scanned
Start
A Ready?
Exchange data with A
Yes
No
B Ready?
Exchange data with B
Yes
No
C Ready?
Exchange data with C
Yes
No

## Slide 9: Interrupt
What is an interrupt?
  Interrupt is an event that CPU temporary stops an executing program in order to execute another one for a request (so-called interrupt request) from I/O;
  The program runs while CPU interrupted call interrupt sub routine (ISR).
  ISRs are stored on ROM and are often used for I/O or controlling I/O devices

## Slide 10: Interrupt vector table (IVT)
8086/8088 has 256 interrupts numbered from 0 to 255
An interrupt vector consists of:
  A number of N, N=0-255 hoặc 00-FFH
  An address of ISR in ROM:
    Code segment (CS)
    Instruction Pointer (IP)
IVT stores the information of all 256 interrupt vectors.

## Slide 11: Interrupt vector table
CS
IP
CS
IP
00
01
FF
Bảng vector ngắt
ROM
Bắt đầu đoạn
Bắt đầu CTCPVN

## Slide 12: Interrupt response of CPU
CTC
CODE
Interrupt request
CPU:
pust FR
disable IF and TF
push CS and IP
get the interrupt route address from IVT
CTCPVN
CTCPVN code
IRET
CPU:
pop IP and CS
pop FR
enable IF and TF
Store shared resgisters
Restore shared registers
Temporary terminates
continue CTC
Notes: D08.1 13.10

## Slide 13: Interrupts
Advantages
  More effective than polling
Disadvantages
  More complicated than polling
  Need more hardware
CPU is subjective to control I/O:

## Slide 14: Direct Memory Access- DMA
CPU handles over for I/O by polling and interrupt.
DMA (Direct Memory Access) allows exchange data between memory and I/O without CPU;
DMA can be suitable for large data size exchanged in short time.
CPU
Memory
I/O
CPU
Memory
I/O
DMAC
Polling and interrupt
DMA

## Slide 15: Direct Memory Access- DMA
DMAC (DMA Controller) takes over CPU for controlling data exchanged between I/O and memory;
DMA is much higher speedy than polling and interrupt. Example (8088):
  It does take 4 clock cycles to transfer 1 byte from I/O to memory for DMA;
  With the same task, it takes up to 39 clock cycles for the use of CPU to exchange data:
    ; clock cycles
    LAP: MOV AL, [SI]; 10
    OUT PORT, AL; 10
    INC SI; 2
    LOOP LAP; 17
    ; Sum: 39 clock cycles

## Slide 16: Direct Memory Access- DMA
CPU
HOLD
Memory
I/O
DMAC
HLDA
DRQ
DACK
System Bus
Notes: D08.2,3 13.10

## Slide 17: Direct Memory Access- DMA
Advantages:
  Effective as data are exchanged in blocks (without CPU);
Disadvantages:
  More complicated than polling and interrupt;
  Need hardware (DMAC)
subjective: I/O